Addresses: Kenbak-uino
0000=A, 0001=B, 0002=X, 0003=PC
0200=Output
0201, 0202 & 0203=Flags A, B & X, b1=Carry, b0=Overflow
0377=Input

Op-codes: octal PQR
----Bit Test & Manipulate----
P-- -Q- --R
0 = Set 0 (bit number)
1 = Set 1
2 = Skip 0 2
3 = Skip 1

----Shifts/Rotates---- (one byte)
P-- -Q- --R
0 = Rt Shift 0/4=A/B:4
1 = Rt Rot 1/5=A/A:1 1
2 = Lt Shift 2/6=A/B:2
3 = Lt Rot 3/7=A/B:3 (bits)

----Misc---- (one byte)
P-- -Q- --R
0 = Halt (don't care) 0
1 = Halt
2 = NOP
3 = NOP 360 = System extension

----Jumps----
P-- -Q- --R
0 = A
1 = B
2 = X
3 = Unc 3 != 0
        4 = JPD 4 == 0
        5 = JPI 5 =< 0
        6 = JMD 6 >= 0
        7 = JMI 7 > 0

----Or, And, LNeg----
P-- -Q- --R
3 0 = Or
        1 = (NOP)
        2 = And
        3 - LNeg (address mode)

----Add, Sub, Load, Store----
P-- -Q- --R
0 = A 0 = Add
1 = B 1 = Sub
2 = X 2 = Load
        3 = Store (address mode)

Address modes; LDA b STA b
3 Const: A=b Immed: (over-write b)
4 Mem: A=[b] [b]=A
5 Ind: A=[[b]] Defer: [[b]]=A
6 Idx: A=[b + X] [b + X]=A
7 Ind/Idx: A=[[b] + X] [[b] + X]=A
Bit Test & Manipulate op-codes are only Mem mode.

Jump Modes; jmp b
4 jmp direct: PC=[b]
5 jmp indirect: PC=[[b]]
6 jmp direct & mark: [b]=PC+2, PC=[b]+1
7 jmp indirect & mark: [[b]]=PC+2, PC=[[b]]+1

System Extension ("NOOP" 0360)
Index in A, b7 clear = read into B, b7 set = write to B
A=
000..007 : DS1307 RTC registers;
  sec,min,hr-24,day,date,month,year,ctrl (BCD).
010 : Flags; b0 set = buttons toggle bits.
011: EEPROM Page Map.
012..016: User data.
017: Control auto-run (see Buttons at Power On).
020: Control LEDs; Read N/A.
  Write b0:INP,b1:ADDR,b2:MEM,b3:RUN,b4-b7=~PWM.
021: Random; Read 0..255, write <seed> or 0.
022: Sleep; Read N/A. Write=delay in ms.
023: Serial byte; @38400baud.
0177: Extensions enabled; Reading sets A=0

Buttons
STOP+CLR: All LEDs off.
CLR+STOR: Zero memory, PC=004, address=004, reset speed.
STOP+BitN: Loads pre-defined program:
  0: Simple counter
  1: Pattern
  2: Counting Clock
  3: BCD Clock
  4: Binary Clock
  5: Das Blinken Lights
  6: Sieve of Eratosthenes
  7: Set RTC (A=HH, B=MM)
BitN+STOR: Write memory to EEPROM page N.
BitN+READ: Reads memory from EEPROM page N. Default pages
  0,1: 256; 2,3: 128; 4,5,67: 64
STOP+READ: System Extension read. Index is address, result in Output.
STOP+STOR: System Extension write. Index is address, value from Input.
BitN+STOP: Set CPU speed. Cycle delay=2^N ms.
BitN+DISP/SET: Send/receive program memory at baud N (0/1/2/3=4800/9600/19k2/38k4)

Buttons at Power On
STOP & BitN: auto-run built-in program N.
READ & BitN: auto-run from EEPROM slot N.
STOP : turn auto-run off.
STOP & CLR : reset configuration to defaults.